## Slide 2: Transient Conduction

## Slide 3
Introduction
Many heat transfer problems are time dependent.
Such unsteady, or transient, problems typically arise when the boundary conditions of a system are changed.
For example, if the surface temperature of a system is altered, the temperature at each point in the system will also begin to change. The changes will continue to occur until a steady-state temperature distribution is reached.
Consider a hot metal rod that is removed from a furnace and exposed to a cool airstream. Energy is transferred by convection and radiation from its surface to the surroundings.
Energy transfer by conduction also occurs from the interior of the metal to the surface, and the temperature at each point in the rod decreases until a steady-state condition is reached.

## Slide 4
Introduction
The nature of the procedure depends on assumptions that may be made for the process. If, for example, temperature gradients within the solid may be neglected, a simple approach, termed the lumped capacitance method, may be used to determine the variation of temperature with time.
Under conditions for which temperature gradients are not negligible, but heat transfer within the solid is one-dimensional, exact solutions to the heat equation may be used to compute the dependence of temperature on both location and time. Such solutions are considered for finite solids, and for semi-infinite solids.
The final properties of the metal will depend significantly on the time-temperature history that results from heat transfer. Controlling the heat transfer is one key in fabricating new materials with enhanced properties.
Our objective in this chapter is to develop procedures for determining the time dependence of the temperature distribution within a solid during a transient process, as well as for determining heat transfer between the solid and its surroundings.

## Slide 5
The Lumped Capacitance Method
Consider a hot metal that is initially at a uniform temperature Ti and is quenched by immersing it in a liquid of lower temperature T∞< Ti (Figure).
If the quenching is said to begin at time t=0, the temperature of the solid will decrease for time t > 0, until it eventually reaches T ∞.
This reduction is due to convection heat transfer at the solid–liquid interface.
The essence of the lumped capacitance method is the assumption that the temperature of the solid is spatially uniform at any instant during the transient process. This assumption implies that temperature gradients within the solid are negligible.

## Slide 6
The Lumped Capacitance Method
From Fourier’s law, heat conduction in the absence of a temperature gradient implies the existence of infinite thermal conductivity.
Such a condition is clearly impossible. However, the condition is closely approximated if the resistance to conduction within the solid is small compared with the resistance to heat transfer between the solid and its surroundings.
The transient temperature response is determined by formulating an overall energy balance on the solid.
This balance must relate the rate of heat loss at the surface to the rate of change of the internal energy.

## Slide 7
The Lumped Capacitance Method
Separating variables and integrating from the initial condition, for which t=0 and T(0)=Ti, we then obtain
where
1
2
Equation 1 may be used to determine the time required for the solid to reach some temperature T, or, Equation 2 may be used to compute the temperature reached by the solid at some time t.

## Slide 8
The Lumped Capacitance Method
where Rt is the resistance to convection heat transfer and Ct is the lumped thermal capacitance of the solid.
Any increase in Rt or Ct will cause a solid to respond more slowly to changes in its thermal environment.
To determine the total energy transfer Q occurring up to some time t, we simply write
Substituting for θ from Equation 2 and integrating, we obtain
The quantity Q is related to the change in the internal energy of the solid. For quenching Q is positive and the solid experiences a decrease in energy.
The quantity (ρVc/hAs) is interpreted as a thermal time constant expressed as

## Slide 9
Validity of the Lumped Capacitance Method
Lumped capacitance method is the simplest and most convenient method that can be used to solve transient heating and cooling problems.
Hence it is important to determine under what conditions it may be used with reasonable accuracy.
consider steady-state conduction through the plane wall of area A (Figure) . Although we are assuming steady-state conditions, this criterion is readily extended to transient processes. One surface is maintained at a temperature Ts,1 and the other surface is exposed to a fluid of temperature T∞< Ts,1. The temperature of this surface will be some intermediate value, Ts,2, for which T∞< Ts,2 < Ts,1 . Hence under steady-state conditions the surface energy balance gives
3

## Slide 10
Validity of the Lumped Capacitance Method
The quantity (hL/k) appearing in Eq 3 is a dimensionless parameter. It is termed the Biot number, and it plays a fundamental role in conduction problems that involve surface convection effects.
The Biot number provides a measure of the temperature drop in the solid relative to the temperature difference between the surface and the fluid.
If Bi<<1, it is reasonable to assume a uniform temperature distribution within a solid at any time during a transient process. the resistance to conduction within the solid is much less than the resistance to convection across the fluid boundary layer. Hence the assumption of a uniform temperature distribution is reasonable.

## Slide 11
Significance of Biot number
Consider the plane wall of Figure 5.4, which is initially at a uniform temperature Ti and experiences convection cooling when it is immersed in a fluid of T∞< Ti.
The problem may be treated as one-dimensional in x, and we are interested in the temperature variation with position and time, T(x, t). This variation is a strong function of the Biot number, and three conditions are shown in Figure.
For Bi<<1, the temperature gradient in the solid is small and T(x, t) ~ T(t). Virtually
all the temperature difference is between the solid and the fluid, and the solid temperature remains nearly uniform as it decreases to T∞.
For moderate to large values of the Biot number, however, the temperature gradients within the solid are significant. Hence T= T(x, t).
For Bi>> 1, the temperature difference across the solid is much larger than that between the surface and the fluid.

## Slide 12
Significance of Biot number
Hence, when confronted with such a problem, the very first thing that one should do is calculate the Biot number.

## Slide 13
If,
the error associated with using the lumped capacitance method is small.
the characteristic length is defined as the ratio of the solid’s volume to surface area, Lc=V/As. this facilitates calculation of Lc for solids of complicated shape.
This reduces to the half-thickness L for a plane wall of thickness 2L, to ro /2 for a long cylinder, and to ro/3 for a sphere.
4
With Lc, the exponent of Eq 2 can be expressed as,
Validity of the Lumped Capacitance Method

## Slide 14
Validity of the Lumped Capacitance Method
Fo is termed the Fourier number. It is a dimensionless time, which, with the Biot number, characterizes transient conduction problems.
5

## Slide 15
Validity of the Lumped Capacitance Method
A thermocouple junction, which may be approximated as a sphere, is to be used for temperature measurement in a gas stream. The convection coefficient between the junction surface and the gas is h =400 W/m2 K, and the junction thermophysical properties are k =20 W/m K, c =400 J/kg.K, and ρ=8500 kg/m3. Determine the junction diameter needed for the thermocouple to have a time constant of 1 s. If the junction is at 25°C and is placed in a gas stream that is at 200°C, how long will it take for the junction to reach 199°C?
EXAMPLE 5.1

## Slide 16
Validity of the Lumped Capacitance Method
EXAMPLE 5.1
Analysis:
Because the junction diameter is unknown, it is not possible to begin the solution by determining whether the criterion for using the lumped capacitance method, Equation 4, is satisfied.
However, a reasonable approach is to use the method to find the diameter and to then determine whether the criterion is satisfied. As = πD2 and V= πD3/6 for a sphere

## Slide 17
Validity of the Lumped Capacitance Method
EXAMPLE 5.1
As, Eq 5 is satisfied (for Lc= ro/3), the lumped capacitance method may be used to an excellent approximation.
2. The time required for the junction to reach T = 199°C is calculated as:

## Slide 18: Evaporators

## Slide 19
Introduction
Evaporation is the removal of solvent as vapor from a solution, slurry or suspension of solid in a liquid.
The aim is to concentrate a non-volatile solute, such as organic compounds, inorganic salts, acids or bases from a solvent.
Common solutes include caustic soda, caustic potash, sodium sulfate, chloride, phosphoric acid, and urea. The most common solvent in most of evaporation systems is water.
Evaporation is normally stopped before the solute starts to precipitate in the operation of an evaporator.
Norbert Rillieux is famous for his invention of the multiple effect pan evaporator for the sugar refining process in 1881.

## Slide 20
Types of Evaporators
Evaporator consists of a heat exchanger for boiling the solution with special provisions for the separation of liquid and vapor phases.
Most of the industrial evaporators have tubular heating surfaces. The tubes may be horizontal or vertical, long or short; the liquid may be inside or outside the tubes.
Short-Tube Vertical Evaporators
Basket-type Vertical Evaporators
Long-Tube Vertical Evaporators
Falling Film Evaporators
Rising or Climbing Film Evaporators
Forced Circulation Evaporators
Agitated Thin Film Evaporator
Gasketed Plate Evaporator

## Slide 21
Types of Evaporators
These are the oldest but still widely used in sugar industry in the evaporation of cane-sugar juice.
Short-tube vertical evaporators consist of a short
tube bundle (about 4 to 10 ft in length) enclosed in a
cylindrical shell. This is called calandria.
The feed is introduced above the upper
tube sheet and steam is introduced to the shell or
steam chest of the calandria.
The solution is heated and partly vaporized in the
tubes.
The central tube in a calandria is of longer diameter.
The circulation rate through the down take is many
times the feed rate. The flow area of the down take
is normally approximately equal to the total tubular
flow area.
Short-tube vertical evaporators

## Slide 22
Types of Evaporators
The construction and operational features of basket-type evaporators are very similar to those of the standard evaporator except that the down take is annular.
The tube bundle with fixed tube sheets forms a basket hung in the center of the evaporator from internal brackets.
The diameter of the tube bundle is smaller than the diameter of the evaporator vessel, thus forming an annular space for the circulation of liquid.
The tube bundle can be removed for the purpose of cleaning and maintenance and thus basket evaporators are more suitable than standard evaporators for scale-forming solutions.
The vapor generated strikes a deflector plate fixed close to the steam pipe that reduces entrained liquid droplets from the vapor.
Basket -type Vertical Evaporators

## Slide 23
Types of Evaporators
This is another most widely employed natural
circulation evaporator because it is often the cheapest
per unit of capacity.
The long vertical tube bundle is fixed with a shell that
extends into a larger diameter vapor chamber at the top.
The evaporator consists of one pass shell and tube HE.
In this type of evaporator, the liquid flows as a thin
film on the walls of long and vertical heated tube. Both
rising film and falling types are used.
The main advantage of this type of evaporator is
higher heat transfer rate. The feed enters at the bottom
and the liquid starts boiling at lower part of the tube.
These are commonly used in concentrating black liquors in the paper and pulp industries.
Long-Tube Vertical Evaporators

## Slide 24
Types of Evaporators
The LTV evaporator is frequently called a rising or climbing film evaporator.
The liquid starts boiling at the lower part of the tube and the liquid and vapor flow upward through the tube.
If the heat transfer rate is significantly higher, the ascending flows generated due to higher specific volume of the vapor-liquid mixture, causes liquid and vapor to flow upwards in parallel flow.
The liquid flows as a thin film along the tube wall. This co-current upward movement against gravity has the advantageous effect of creating a high degree of turbulence in the liquid.
This is useful during the evaporation of highly viscous and fouling solutions.
Rising or Climbing Film Evaporators

## Slide 25
Types of Evaporators
The liquid is fed at the top of the tubes in a vertical tube
bundle.
The liquid is allowed to flow down through the inner wall
of the tubes as a film.
As the liquid travels down the tubes the solvent vaporizes
and the concentration gradually increases.
Vapor and liquid are usually separated at the bottom of the
tubes and the thick liquor is taken out.
Evaporator liquid is recirculated through the tubes by a
pump below the vapor-liquid separator.
The distribution of liquid in the inner wall of the tubes
greatly affects the performance of this type of evaporator.
They are used for the concentration of fruit juices and heat sensitive materials because of the low holdup time. The device is suitable for scale-forming solutions as boiling occur on the surface of the film.
Falling Film Evaporators

## Slide 26
Types of Evaporators
These are usually more costly than natural circulation evaporators.
However, the natural circulation evaporators are not suitable under some situations such as:
Highly viscous solutions due to low heat transfer coefficient
Solution containing suspended particles
For heat sensitive materials
All these problems may be overcome when the liquid is circulated at high velocity through the heat exchanger tubes to enhance the heat transfer rate and inhibit particle deposition.
Any evaporator that uses pump to ensure higher circulation velocity is called a forced circulation evaporator.
The main components of a forced circulation evaporator are a tubular shell and tube heat exchanger (either horizontal or vertical), a flash chamber (separator) mounted above the heat exchanger and a circulating pump.
Forced Circulation Evaporators

## Slide 27
Types of Evaporators
The solution is heated in the heat exchanger without boiling and the superheated solution flashes off (partially evaporated) at a lower pressure are reduced in the flash chamber.
The pump pumps feed and liquor from the flash chamber and forces it through the heat exchanger tubes back to the flash chamber.
Forced circulation evaporator is commonly used for the concentration of caustic and brine solutions and also in evaporation of the corrosive solution.
Forced Circulation Evaporators

## Slide 28
Types of Evaporators
This evaporator consists of a vertical steam-jacketed cylinder and the feed solution flows down as a film along the inner surface of large diameter jacket.
Liquid is distributed on the tube wall by a rotating assembly of blades mounted on a shaft placed coaxially with the inner tube.
The blades maintain a close clearance of around 1.5 mm or less from the inner tube wall.
The main advantage is that rotating blades permit handling of extremely viscous solutions.
The device is suitable to concentrate solutions having viscosity as high as up to 100 P.
Agitated Thin Film Evaporator

## Slide 29
Types of Evaporators
The gasketed-plate evaporator is also called the plate evaporator because the design is similar to that of a plate heat exchanger.
A number of embossed plates with four corner openings are mounted by an upper and a bottom carrying bar.
The gasket is placed at the periphery of the plates. The interfering gaskets of two adjacent plates prevent the mixing of the fluids and lead the fluid to the respective flow path through the corner opening.
The fluids may either flow in series or parallel depending on the gasket arrangement. The heat transfer coefficient is greatly enhanced due to high turbulent flow through narrow passages.
This evaporator is suitable for highly viscous, fouling, foaming and heat sensitive solutions. This type of evaporators is mainly used for concentration of food products, pharmaceuticals, emulsions, glue, etc.
Gasketed Plate Evaporator

## Slide 30
Methods of Feeding of Evaporators
Evaporators are classified by the number of effects. In case of a single-effect evaporator, the vapor from the boiling liquor is condensed and the concentrated product is withdrawn from the bottom of the evaporator.
Although the operation is simple, the device does not use steam efficiently. Typically 1.1 to 1.3 kg of steam is required to evaporate 1 kg of water.
The steam consumption per unit mass of water evaporated can be increased by putting more than one evaporator in series such that the vapor from one evaporator is used in the second evaporator for heating.
The vapor from the second evaporator is condensed and the arrangement is called double-effect evaporator. The heat from the vapor generated in the first evaporator is used in the second evaporator.
Evaporation of water is nearly doubled in a double effect evaporation system compared to a single effect per unit mass of steam used.
There are several configurations based on feeding arrangement.

## Slide 31
Methods of Feeding of Evaporators
The typical feeding method of multi-effect evaporators is forward. Both feed and steam are introduced in the first effect and the feed passed from effect to effect parallel to the vapor from the earlier effect.
Concentration increases from the first effect to the last. Forward feeding operation is helpful when the concentrated product may degenerate if exposed to high temperatures.
The product is withdrawn from the last effect. It requires a pump for feeding of dilute solution to the first effect. A pump removes thick liquor from the last effect.
The liquid from one effect to the next effect also can be transferred without a pump as the flow occurs in the direction of decreasing pressure.
Forward feed

## Slide 32
Methods of Feeding of Evaporators
In backward feed configuration, the feed enters at the last effect (coldest effect) and is pumped through the successive effects.
The product is withdrawn from the first effect (hottest) where the steam is introduced . This method of feeding requires a pump between each pair of effects to transfer liquid from lower pressure effects to higher-pressure effects.
It is advantageous when cold feed entering needs to be heated to a lower temperature than in forward feed operation.
Backward feed is commonly used when products are viscous and exposure to higher temperature increases the rate of heat transfer due to reduction in viscosity of the liquid.
Backward feed

## Slide 33
Methods of Feeding of Evaporators
In the mixed feed operation, the dilute feed liquid enters at an intermediate effect and flows in the next higher effect till it reaches the last effect of the series.
In this section, liquid flows in the forward feed mode. Partly concentrated liquor is then pumped back to the effect before the one to which the fresh feed was introduced for further concentration.
Mixed feed arrangement eliminates some of the pumps needed in the backward configuration as flow occurs due to pressure difference whenever applicable.
Mixed feed
The fresh feed is introduced to each effect and in this configuration, the product is withdrawn of from the same effect in parallel feed operation.
There is no transfer of liquid from one effect to another effect. It is used primarily when the feed is saturated and the product is a solid-containing slurry. This is most common in crystallizing evaporators.
Parallel feed

## Slide 34
Methods of Feeding of Evaporators

## Slide 35
Performance of Evaporators
The performance of a steam-heated evaporator is measured in terms of its capacity and economy.
Capacity is defined as the number of kilogram of water vaporized per hour.
Economy (or steam economy) is the number kilogram of water vaporized from all the effects per kilogram of steam used.
For single effect evaporator, the steam economy is about 0.8 (<1).
The capacity is about n-times that of a single-effect evaporator and the economy is about 0.8n for an n-effect evaporator.
However, pumps, interconnecting pipes and valves are required for the transfer of liquid from one effect to another effect which increases both equipment and operating costs.

## Slide 36: Radiation: Processes and Properties

## Slide 37
Introduction
It is an extremely important process, and in the physical sense it is perhaps the most interesting of the heat transfer modes.
It is relevant to many industrial heating, cooling, and drying processes, as well as to energy conversion methods that involve fossil fuel combustion and solar radiation.
In this chapter our objective is to consider the means by which thermal radiation is generated, the specific nature of the radiation, and the manner in which it interacts with matter.

## Slide 38
Fundamental Concepts
Consider a solid that is initially at a higher temperature Ts than that of its surroundings
Tsur, but around which there exists a vacuum (Figure).
The presence of the vacuum precludes energy loss from the surface of the solid by conduction or convection. However, the solid will cool and eventually achieve thermal equilibrium with its surroundings.
This cooling is associated with reduction in the internal energy stored by the solid and is a direct consequence of the emission of thermal radiation from the surface.
The surface will intercept and absorb radiation
originating from the surroundings. However, if
Ts > Tsur the net heat transfer rate by radiation
qrad,net is from the surface, and the surface will
cool until Ts reaches Tsur.

## Slide 39
Fundamental Concepts
The thermal radiation is the rate at which energy is emitted by matter as a result of its finite temperature.
At this moment thermal radiation is being emitted by all the matter that surrounds you: by the furniture and walls of the room, if you are indoors, or by the ground, buildings, and the atmosphere and sun if you are outdoors.
The mechanism of emission is related to energy released as a result of oscillations or transitions of the many electrons that constitute matter.
These oscillations are sustained by the internal energy, and therefore the temperature, of the matter. Hence we associate the emission of thermal radiation with thermally excited conditions within the matter.
All forms of matter emit radiation. For gases and for semitransparent solids, such as glass and salt crystals at elevated temperatures, emission is a volumetric phenomenon.
That is, radiation emerging from a finite volume of matter is the integrated effect of local emission throughout the volume.

## Slide 40
Fundamental Concepts
we concentrate on situations for which radiation is a surface phenomenon.
In most solids and liquids, radiation emitted from interior molecules is strongly absorbed by adjoining molecules.
Accordingly, radiation that is emitted from a solid or a liquid originates from molecules that are within a distance of approximately 1μm from the exposed surface.
It is for this reason that emission from a solid or a liquid into an adjoining gas or a vacuum can be viewed as a surface phenomenon.
Radiation originates due to emission by matter and that its subsequent transport does not require the presence of any matter. But what is the nature of this transport?
Radiation may be viewed as the propagation of electromagnetic waves.
Radiation is attributed to the standard wave properties of frequency ν and wavelength λ .
For radiation propagating in a particular medium, the two properties are related by
where c is the speed of light in the medium.

## Slide 41
Fundamental Concepts
For propagation in a vacuum, co= 2.998 X 108 m/s.
The unit of wavelength is commonly the micrometer (μm), where 1μm=106 m.

## Slide 42
Fundamental Concepts
The short wavelength gamma rays, X rays, and ultraviolet (UV) radiation are primarily of interest to the high-energy physicist and the nuclear engineer.
The long wavelength microwaves and radio waves ( 105 m) are of concern to the electrical engineer.
The intermediate portion of the spectrum, which extends from approximately 0.1 to 100 m and includes a portion of the UV and all of the visible and infrared (IR), that is termed thermal radiation because it is both caused by and affects the thermal state or temperature of matter. For this reason, thermal radiation is pertinent to heat transfer.

## Slide 43
Radiation Intensity
Radiation that leaves a surface can propagate in all possible directions.
Radiation incident upon a surface may come from different directions, and the manner in which the surface responds to this radiation depends on the direction.
Such directional effects can be of primary importance in determining the net radiative heat transfer rate and may be treated by introducing the concept of radiation intensity.
Due to its nature, mathematical treatment of radiation heat transfer involves the extensive use of the spherical coordinate system.
From Figure a, the differential plane angle dα is defined by a region between the rays of a circle and is measured as the ratio of the arc length dl on the circle to the radius r of the circle.
Similarly, from Figure b, the differential solid angle dω is defined by a region between the rays of a sphere and is measured as the ratio of the area dAn on the sphere to the sphere’s radius squared.

## Slide 44
Radiation Intensity

## Slide 45
Radiation Intensity
Consider emission in a particular direction from an element of surface area dA1, as shown in Figure c.
The direction may be specified in terms of the zenith and azimuthal angles, θ and ϕ, respectively, of a spherical coordinate system (Figure d).

## Slide 46
Radiation Intensity
The area dAn, through which the radiation passes, subtends a differential solid angle dω when viewed from a point on dA1.
As shown in Figure, the area dAn is a rectangle of dimension r dθ X r sinθ dϕ; thus,
dAn= r2 sinθ dθ dϕ.
12.3
the unit of the solid angle is the steradian (sr)

## Slide 47
Radiation Intensity
From Figure c, let’s consider the rate at which emission from dA1 passes through dAn. This quantity may be expressed in terms of the spectral intensity I λ,e of the emitted radiation.
Iλ,e is defined as the rate at which radiant energy is emitted at the wavelength λ in the (θ, ϕ) direction, per unit area of the emitting surface normal to this direction, per unit solid angle about this direction, and per unit wavelength interval d λ about λ. units :W/m2 .sr. μm,
Note: The area used to define the intensity is the component of dA1 is perpendicular to the direction of the radiation. From Figure, we see that this projected area is equal to dA1 cosθ
The spectral intensity is
where (dq/dλ)= dqλ is the rate at which radiation of wavelength leaves dA1 and passes through dAn.

## Slide 48
Radiation Intensity
Rearranging above Equation, it follows that
This important expression allows us to compute the rate at which radiation emitted by a surface propagates into the region of space defined by the solid angle d about the (θ, ϕ) direction.
However, to compute this rate, the spectral intensity Iλ,e of the emitted radiation must be known.
Expressing Equation 12.6 per unit area of the emitting surface and substituting from Equation 12.3, the spectral radiation flux associated with dA1 is
12.6
the spectral, hemispherical emissive power E (W/m2 .m) is defined as the rate at which radiation of wavelength λ is emitted in all directions from a surface per unit wavelength interval dλ about λ and per unit surface area.

## Slide 49
Radiation Intensity
Thus, E λ is the spectral heat flux associated with emission into a hypothetical hemisphere above dA1.
Note :Eλ is a flux based on the actual surface area, whereas I λ,e is based on the projected area. The cosθ term appearing is a consequence of this difference.
The total, hemispherical emissive power, E (W/m2), is the rate at which radiation is emitted per unit area at all possible wavelengths and in all possible directions.
from Equation 12.8

## Slide 50
Radiation Intensity
Let us consider a diffuse emitter as a surface for which the intensity of the emitted radiation is independent of direction, in which case Removing Iλ,e from the integrand of Equation 12.8 and performing the integration, it follows that
Similarly, from Equation 12.10
where Ie is the total intensity of the emitted radiation

## Slide 51
Radiation Intensity
EXAMPLE 12.1
A small surface of area A1=10-3 m2 is known to emit diffusely, and from measurements
the total intensity associated with emission in the normal direction is In = 7000 W/m2.sr.
Radiation emitted from the surface is intercepted by three other surfaces of area A2= A3= A4 = 10-3 m2, which are 0.5 m from A1 and are oriented as shown. What is the intensity associated with emission in each of the three directions? What are the solid angles subtended by the three surfaces when viewed from A1? What is the rate at which radiation emitted by A1 is intercepted by the three surfaces?

## Slide 52
Radiation Intensity
EXAMPLE 12.1
SOLUTION
Known: Normal intensity of diffuse emitter of area A1 and orientation of three surfaces relative to A1.
Find:
Intensity of
emission in each of
the three directions.
2. Solid angles
subtended by the
three surfaces.
3. Rate at which
radiation is intercepted
by the three surfaces.

## Slide 53
Radiation Intensity
EXAMPLE 12.1
1. From the definition of a diffuse emitter, we know that the intensity of the emitted radiation is independent of direction. Hence I=7000 W/m2. sr for each of the three directions.
2. Treating A2, A3, and A4 as differential surface areas, the solid angles may be computed from
where dAn is the projection of the surface normal to the direction of the radiation. Since surfaces A3 and A4 are normal to the direction of radiation, the solid angles subtended by these surfaces can be directly found from this equation as
Since surface A2 is not normal to the direction of radiation, we use dAn,2 = dA2 cosθ2, where θ2 is the angle between the surface normal and the direction of the radiation. Thus

## Slide 54
Radiation Intensity
EXAMPLE 12.1
3. The rate at which radiation is intercepted by each of the three surfaces may be found from Equation 12.6, which, for the total radiation, may be expressed as
where θ1 is the angle between the normal to surface 1 and the direction of the radiation. Hence,

## Slide 55
Spectral Irradiation
The intensity of the incident radiation is related to an important radiative flux, termed the irradiation, which encompasses radiation incident from all directions.
The spectral irradiation Gλ (W/m2.μm) is defined as the rate at which radiation of wavelength is incident on a surface, per unit area of the surface and per unit wavelength interval dλ about λ.
The cosθ factor originates because Gλ is a flux based on the actual surface area, whereas Iλ,i is defined in terms of the projected area.
If the total irradiation G (W/m2) represents the rate at which radiation is incident per unit area from all directions and at all wavelengths, it follows that

## Slide 56
Spectral Irradiation
From Equation 12.13
If the incident radiation is diffuse, Iλ,i is independent of θ and ϕ, then

## Slide 57
Spectral Irradiation
EXAMPLE 12.2
The spectral distribution of surface irradiation is as follows:
What is the total irradiation?

## Slide 58
Spectral Irradiation
EXAMPLE 12.2
SOLUTION
Known: Spectral distribution of surface irradiation.
Find: Total irradiation.
Analysis: The total irradiation may be obtained from Equation 12.14
The integral is evaluated by breaking it into parts.

## Slide 59
Radiosity
The term Radiosity, accounts for all the radiant energy leaving a surface. Since this radiation includes the reflected portion of the irradiation, as well as direct emission (Figure), the radiosity is generally different from the emissive power.
The spectral radiosity Jλ (W/m2.μm) represents the rate at which radiation of wavelength leaves a unit area of the surface, per unit wavelength interval d λ about λ.
Since it accounts for radiation leaving in all directions, it is related to the intensity associated with emission and reflection, I λ,e+r (λ, θ, ϕ ), by the expression

## Slide 60
Radiosity
Hence the total radiosity J (W/m2) associated with the entire spectrum is
If the surface is both a diffuse reflector and a diffuse emitter, I,e+r is independent of θ and ϕ , and it follows that

## Slide 61
Black Body Radiation
To evaluate the emissive power, irradiation, or radiosity of a real surface, we must quantify the spectral intensities used in Equations 12.8, 12.13, and 12.18.
To do so, it is useful and necessary to first introduce the concept of a blackbody.
A blackbody absorbs all incident radiation, regardless of wavelength and direction.
2. For a prescribed temperature and wavelength, no surface can emit more energy than a blackbody.
3. Although the radiation emitted by a blackbody is a function of wavelength and temperature, it is independent of direction. That is, the blackbody is a diffuse emitter.
Although closely approximated by some surfaces, it is important to note that no surface has precisely the properties of a blackbody.
The closest approximation is achieved by a cavity whose inner surface is at a uniform temperature. If radiation enters the cavity through a small aperture ,it is likely to experience many reflections before reemergence. Hence it is almost entirely absorbed by the cavity, and blackbody behavior is approximated.

## Slide 62
Black Body Radiation
Since blackbody emission is diffuse, the spectral intensity Iλ,b of radiation leaving the cavity is
independent of direction.
Any small surface in the cavity experiences irradiation for which Gλ = E λ,b(λ, T ).
This surface is diffusely irradiated, regardless of its orientation. Blackbody radiation exists within the cavity irrespective of whether the cavity surface is highly reflecting or absorbing.
The Planck Distribution
The blackbody spectral intensity first been determined by Planck . It is given by
h= 6.626X 10-34 J.s universal Planck Constant
k=1.381X10-23 J/K Boltzmann constants
co= 2.998X108 m/s the speed of light in vacuum
T is the absolute temperature of the blackbody (K)

## Slide 63
Black Body Radiation
The Planck Distribution
Since the blackbody is a diffuse emitter, its spectral emissive power is given by
the first and second radiation constants are given by
Equation 12.24, known as the Planck distribution

## Slide 64
Black Body Radiation
Wien’s Displacement Law
It is known that the blackbody spectral distribution has a maximum and that the corresponding wavelength λmax depends on temperature.
The nature of this dependence may be obtained by differentiating Equation 12.24 with respect to λ and setting the result equal to zero. we obtain,
where the third radiation constant is C3= 2898 μm.K.
Equation 12.25 is known as Wien’s displacement law.
According to this result, the maximum spectral emissive power is displaced to shorter wavelengths with increasing temperature.

## Slide 65
Black Body Radiation
The Stefan–Boltzmann Law
Substituting the Planck distribution, Equation 12.24, into Equation 12.9,
the total emissive power of a blackbody Eb is expressed as
Performing the integration,
Stefan–Boltzmann constant, σ = 5.670X10-8 W/m2. K4
This result is termed the Stefan–Boltzmann law.
It enables calculation of the amount of radiation emitted in all directions and over all wavelengths from knowledge of the temperature of the blackbody.
The total intensity associated with blackbody emission is

## Slide 66
Black Body Radiation
Band Emission
It is often necessary to know the fraction of the total emission from a blackbody that is in a certain wavelength interval or band.
For a prescribed temperature and the interval from 0 to λ , this fraction is determined by the ratio of the shaded section to the total area under the curve of Figure. Hence,
It can also be used to obtain the fraction of the radiation between any two wavelengths λ1 and λ2, as

## Slide 67
Black Body Radiation
Band Emission

## Slide 68
Black Body Radiation
Band Emission

## Slide 69
Black Body Radiation
Band Emission
The blackbody functions are listed in the third and fourth columns of Table 12.1.
The third column facilitates calculation of the spectral intensity for a prescribed wavelength and temperature. This quantity is obtained by simply multiplying the tabulated value of Iλ,b/σT5 by σ T5.
The fourth column is used to obtain an estimate of the ratio of the spectral intensity at any wavelength to that at λmax.
EXAMPLE 12.3
Consider a large isothermal enclosure that is maintained at a uniform temperature of 2000 K. Calculate the emissive power of the radiation that emerges from a small aperture on the enclosure surface. What is the wavelength λ1 below which 10% of the emission is concentrated? What is the wavelength λ2 above which 10% of the emission is concentrated? Determine the maximum spectral emissive power and the wavelength at which this emission occurs. What is the irradiation incident on a small object placed inside the enclosure?
Table 12.1 can be seen in the text book Pg No.741!!

## Slide 70
Black Body Radiation
EXAMPLE 12.3
SOLUTION
Known: Large isothermal enclosure at uniform temperature.
Find:
1. Emissive power of a small aperture on the enclosure.
2. Wavelengths below which and above which 10% of the radiation is concentrated.
3. Spectral emissive power and wavelength associated with maximum emission.
4. Irradiation on a small object inside the enclosure.

## Slide 71
Black Body Radiation
EXAMPLE 12.3
Analysis:
1. Emission from the aperture of any isothermal enclosure will have the characteristics of blackbody radiation. Hence,
2. The wavelength λ1 corresponds to the upper limit of the spectral band (0 → λ1) containing 10% of the emitted radiation. With F(0 → λ1)= 0.10 it follows from Table 12.1 that
λ1T= 2195 μm. K. Hence,
λ1= 1.1 μm
Use interpolation formula to solve λ1T

## Slide 72
Black Body Radiation
EXAMPLE 12.3
It follows from Table 12.1 that λ2T= 9382 μm. K. Hence
The wavelength λ2 corresponds to the lower limit of the spectral band (λ2 → ∞) containing 10% of the emitted radiation. With
The spectral emissive power associated with this wavelength may be computed from the third column of Table 12.1.
For λmaxT= 2898μ m. K

## Slide 73
Black Body Radiation
EXAMPLE 12.3
Since the emission is diffuse,
4. Irradiation of any small object inside the is calculated as being equal to emission from a blackbody at the enclosure surface temperature. Hence G= Eb(T), in which case G=E

## Slide 74
Black Body Radiation
EXAMPLE 12.4
A surface emits as a blackbody at 1500 K. What is the rate per unit area (W/m2) at which it emits radiation over all directions corresponding to 0°≤ θ ≤ 60° and over the wavelength interval 2μm ≤ λ ≤ 4 μm?
SOLUTION
Known: Temperature of a surface that emits as a blackbody.
Find: Rate of emission per unit area over all directions between θ= 0° and θ= 60°
and over all wavelengths between λ= 2 and 4 μm.
Analysis: The desired emission may be inferred from Equation 12.10, with the limits of integration restricted as follows:
since a blackbody emits diffusely,

## Slide 75
Black Body Radiation
EXAMPLE 12.4
Substituting from Equation 12.11 and multiplying and dividing by Eb, this result may be put in a form that allows for use of Table 12.1 in evaluating the spectral integration. In particular,

## Slide 76
Black Body Radiation
EXAMPLE 12.4
from Table 12.1
Hence
From Equation 12.26, it then follows that

## Slide 77
Emission from Real Surfaces
A blackbody is taken as a reference in describing emission from a real surface.
A surface radiative property known as the emissivity is defined as the ratio of the radiation emitted by the surface to the radiation emitted by a blackbody at the same temperature.
We define the spectral, directional emissivity ελ,θ (λ, θ, ϕ, T ) of a surface at the temperature T as the ratio of the intensity of the radiation emitted at the wavelength λ and in the direction of θ and ϕ to the intensity of the radiation emitted by a blackbody at the same values of T and λ .
a total, directional emissivity εθ , which represents a spectral average of ελ,θ, may be defined as

## Slide 78
Emission from Real Surfaces
A spectral, hemispherical emissivity is defined as
The total, hemispherical emissivity, which represents an average over all possible directions and wavelengths, is defined as
Derivation in pg No: 746 !!

## Slide 79
Emission from Real Surfaces
EXAMPLE 12.5
A diffuse surface at 1600 K has the spectral, hemispherical emissivity shown as follows.
Determine the total, hemispherical emissivity and the total emissive power.
SOLUTION
Known: Spectral, hemispherical emissivity of a diffuse surface at 1600 K.

## Slide 80
Emission from Real Surfaces
EXAMPLE 12.5
Find:
1. Total, hemispherical emissivity.
2. Total emissive power.
3. Wavelength at which spectral emissive power will be a maximum.
Analysis:
1. The total, hemispherical emissivity is given by Equation 12.36, where the integration is performed in parts as follows:

## Slide 81
Emission from Real Surfaces
EXAMPLE 12.5
2. The total emissive power is

## Slide 82
Environmental Radiation
The sun is a spherical radiation source that is 1.39 X 109 m in diameter and is located 1.50 X1011 m from the earth. The sun emits approximately as a blackbody at 5800 K.
As the radiation emitted by the sun travels through space, the radiation flux decreases because of the greater (spherical) area through which it passes.
At the outer edge of the earth’s atmosphere, the flux of solar energy has decreased by a factor of (rs /rd)2, where rs is the radius of the sun and rd is the distance from the sun to the earth.
The solar constant, Sc, is defined as the flux of solar energy incident on a surface oriented normal to the sun’s rays, at the outer edge of the earth’s atmosphere, when the earth is at its mean distance from the sun (Figure). It has a value of Sc= 1353 W/m2.
For a horizontal surface(that is, parallel to earth’s surface), solar radiation appears as a beam of nearly parallel rays that form an angleθ , the zenith angle, relative to the surface normal.

## Slide 83
Environmental Radiation
The extraterrestrial solar irradiation GS,o, defined for a horizontal surface, depends on the geographic latitude, as well as the time of day and year. It may be determined from an expression of the form
The quantity f is a small correction factor to account for the eccentricity of the earth’s orbit about the sun (0.97≤ f ≤ 1.03)
As solar radiation passes through the earth’s atmosphere, its magnitude and its spectral and directional distributions experience significant change.
The change is due to absorption and scattering of the radiation by the atmospheric constituents.

## Slide 84
Environmental Radiation
Atmospheric scattering provides for redirection of the sun’s rays and consists of two kinds (Figure).
Rayleigh (or molecular) scattering by very small gas molecules occurs when the ratio of the effective molecule diameter to the wavelength of the radiation, πD/λ, is much less than unity and provides for nearly uniform scattering of radiation in all directions.
Hence, half of the scattered
radiation is redirected to space,
while the remaining portion strikes
the earth’s surface. At any point on this
surface, the scattered radiation is
incident from all directions.
In contrast, Mie scattering by larger dust and aerosol
particles of the atmosphere occurs when πD/λ is
approximately unity and is concentrated in directions
that are close to that of the incident rays.
Hence virtually all this radiation strikes
the earth’s surface in directions close
to that of the sun’s rays.

## Slide 85
Environmental Radiation
The cumulative effect of the scattering processes on the directional distribution of solar radiation striking the earth’s surface is shown in Figure a.
That portion of the radiation that has penetrated the atmosphere without having been scattered
(or absorbed) is in the direction of the zenith angle and is termed the direct radiation.
The scattered radiation is incident from all directions, However, because the radiation intensity is often assumed to be independent of direction (Figure b), it is termed diffuse.
The total solar radiation reaching the earth’s surface
is therefore the sum of direct and diffuse contributions.
The emissive power associated with the earth’s surface is
where ε and T are the surface emissivity and temperature, respectively
ε of water = 0.97

## Slide 86
Environmental Radiation
Earth irradiation due to atmospheric emission is expressed as
where Tsky is the effective sky temperature. Its value depends on atmospheric conditions
EXAMPLE 12.11
A flat-plate solar collector with no cover plate has a selective absorber surface of emissivity 0.1 and solar absorptivity 0.95. At a given time of day the absorber surface temperature Ts is 120°C when the solar irradiation is 750 W/m2, the effective sky temperature is -10°C, and the ambient air temperature T∞ is 30°C. Assume that the heat transfer convection coefficient for the calm day conditions can be estimated from
Calculate the useful heat removal rate (W/m2) from the collector for these conditions. What is the corresponding efficiency of the collector?

## Slide 87
Environmental Radiation
EXAMPLE 12.11
SOLUTION
Known: Operating conditions for a flat-plate solar collector.
Analysis:
1. Performing an energy balance on the absorber,
or, per unit surface area,

## Slide 88
Environmental Radiation
EXAMPLE 12.11
Since the sky radiation is concentrated in approximately the same spectral region as that of surface emission, let’s assume
2. The collector efficiency, defined as the fraction of the solar irradiation extracted as useful energy, is then